## Slide 1
Lecture 7: From Pass Transistor Logic to Transmission Gate
Notes: 上一节：如何利用晶体管作为switch的性质来传输信号
仅用一个NMOS来作信号传输的问题：pull up时摆幅无法从0-VDD
针对单个NMOS或单个PMOS组成的缺点，如何解决

## Slide 2: Review: 2-Input XOR Gate
A | B | F
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
A
B controls A
A
PTL 2-input XOR Gate
Such circuit design strategy can be easily expand to any N-input logic gates.
PTL相比互补CMOS在实现某些功能的电路更加方便，使用晶体管的数量更少。
——但也会带来其他问题。
Still 4 Transistors in Total!

## Slide 3: Review: NMOS-Only Switch Issue
The voltage at Y can only be pulled-up to VDD – VTN
If |VTP| of M2 is smaller than VTN, then M2 cannot be turned off.  Static power consumption
Also the smaller VGS of M1 reduces the discharge current.
 Longer discharge time
𝑨 = 𝑽
𝑫𝑫
𝑿: 𝟎𝑽𝑫𝑫
𝒀
S
D
M1
M2
𝑭
Notes: PTL的弊端，后考虑如何解决
如果设计不好，Y不够大，无法把M2关断

## Slide 4: Improvement Strategy #1
The level restoring PMOS transistor forms
a positive feedback.
𝑿: 𝟎𝑽𝑫𝑫
𝒀: 𝟎𝑽𝑫𝑫 − 𝑽𝑻𝑵
1
M Turn ON
𝑭: 𝑽𝑫𝑫𝟎
M4
Turn ON
𝒀: 𝑽𝑫𝑫 − 𝑽𝑻𝑵  𝑽𝑫𝑫
Realize Full Voltage Swing
电平恢复器
Notes: 方法1：电平恢复
使用一个PMOS作为电平恢复器；优点：所有电平不是GND就是VDD，没有静态功耗
Y受到了两路电路，从M4所在支路，Y可以被上拉到VDD
正反馈，将M2彻底关闭，M1打开
接下来看其会不会导致什么其他影响

## Slide 5: Racing Issue at Point Y
𝑨 = 𝑽𝑫𝑫
𝒀
M1
M
2
𝑭
M3
M
4
𝑿
𝑽𝑫𝑫𝟎
At t = 0
  Y = VDD, F = 0
  M1, M4 ON, M2 , M3 OFF
t>0，M1,M3 ,M4 ON, M2 OFF
At t > 0, equivalent circuit
M4
M3
𝒀
3
Y
DD
Ron,M
V
𝑭 V 
Ron,M  Ron,M
3 4
If WM4 is too large (Ron,M4 is too small), VY cannot be pulled below VTN* (i.e., M1 turned OFF)*, the logic function cannot be operated correctly.
Notes: 此时M1，M4导通，对于M3，由于X,Y,A都是VDD，因此是处于关断状态
当X->0后，M3导通，这时候Y也降
此时Y的电压就受到M3和M4电阻影响，V(Y)就会变大

## Slide 6: M4 PMOS Sizing Effect
Node Y stops discharging and the inverter never switches any more.
Desired fast switching
Logic function can be implemented, yet with longer time.  need to avoid.
Level restoring method has speed and power impacts: increases the capacitance at Y, and slows down the propagation delay.
Notes: 会丧失应有的性能，如：无法快速放电
具体看会有什么影响，M4的W很小，理想
但是很大时，无法下拉，功能受影响

## Slide 7: Weak and Strong PUN & PDN
C
L
D
CL
V
DD
S
D
VDD  0
NMOS passes a STRONG 0 in pull- down network (PDN)
C
L
D
S
VDD
VDD
0  VDD - VTn
NMOS passes a WEAK 1 in pull-up network (PUN)
VGS  VTn
VSG  VTp
S
PMOS passes a WEAK 0 in pull- down network (PDN)
CL
S
PMOS passes a STRONG 1 in pull- up network (PUN)
VDD  |VTp|
VDD
D
0  VDD
Notes: 方法2：使用PMOS来进行pull-up
之前不行，原因是NMOS无法强上拉

## Slide 8: Improvement Strategy #2
NMOS and PMOS in parallel
When A: 0  VDD
PMOS helps to pull-up Y to VDD
When A: 0  VDD
NMOS helps to pull-down Y to GND
Transmission Gate (TG)
TG enables bi-directional rail-to-rail switching.
TG requires two transistors with more control signals than PTL.
Symbol
解决电压损失问题最广泛使用的方法是使用传输门（Transmission Gate ，TG）
Notes: 核心思想依旧是PTL
实现功能需要更多的晶体管
X与Y是对偶的

## Slide 9: Example: TG-Based XOR
将NMOS替换为TG
各需要多少个晶体管？
Notes: 遇到单个NMOS就将其补全为TG

## Slide 10: Example: TG-Based XOR
A | B | F
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
A
B controls A
A
TG 2-input XOR Gate
Simplest version – Make use of the bi-directional feature of TG
各需要多少个晶体管？如果使用互补CMOS设计，需要多少个晶体管？
Notes: 6个晶体管（互补CMOS需要12个）
解决了问题，同时总体需要增加的晶体管数也减少了

## Slide 11: Example: TG-Based XOR
各需要多少个晶体管？如果使用互补CMOS设计，需要多少个晶体管？
Notes: 6个晶体管（互补CMOS需要12个）
解决了问题，同时总体需要增加的晶体管数也减少了

## Slide 12: Equivalent Resistance of TG
𝑽𝑫𝑫
0
𝒀
𝑽𝑫𝑫
Transmission Gate (TG)
VY (V)
Sp
Dn
Dp
Sn
I
|VGSp| = VDD
VGSn = VDD - VY
考虑当TG用于上拉时的等效电阻
Notes: 等效电阻的大小
电流分析：电流方向为正电子（即空穴）的方向
虽然S，D相反，但是电流方向相同
电阻分析：

## Slide 13: Equivalent Resistance of TG
TG with equal PMOS and NMOS
KEY: We need to consider the penalty for weak transition: NMOS-PUN & PMOS-PDN
*In this course, we assume penalty factor is  = 2
由于在这些情况下，相应的等效电阻都会更大，所以加入来模拟
PUN
Strong PMOS, Weak NMOS
W – 2R0
W – R0
PDN
Strong NMOS, Weak PMOS
W – 2R0
W – R0
RON,PUN = R0
(=2)
RON,PDN = 0.8R0 (=2)
Equal Strength
RON ~ R0
粗略地近似，将其视为相等
Notes: 当α=2时

## Slide 14: Logical Efforts of a TG Gate
KEY: ALWAYS trace back to VDD (PUN) or GND(PDN) to form a complete charge/discharge path!
PUN Gate Sizing
RON,M2 + RON,TG = R0  RON,TG = R0/2 & RON,TG = R0/2
PDN Gate Sizing
RON,M1 + RON,TG = R0  RON,TG = R0/2 & RON,TG = R0/2
gA = 6/3 = 2
gS = 2/3
Drawbacks: Neglecting the parasitic capacitance at Y.
通常计算PDN或者PUN的传播延时时都以VDD或者GND作为基准
Notes: 从传播延时的定义出发一般将其视为一级的电路。
作为一级电路时的问题：充电时，V(Y)未知
误差，Y的电容被忽略

## Slide 15: Example: TG-Based Logic Circuit
1
1
1
1
Calculate the worst-case delay of this circuit.
若应用Logical Effort方法分析，
该如何对此电路进行分级？
Notes: 依照前面的例子，将TG与前一个门视为同一级

## Slide 16: Example: TG-Based Logic Circuit
Stage 1
Stage 2
Stage 3
g1 = 5/3
g2 = 2
g3 = 1
1
1
1
1
CMOS
CMOS
Notes: 可以根据新得到的分级计算Logic effort

## Slide 17
希望大家给五星满分好评！