## Slide 1
Lecture 8: Adders
Circuit Implementation 1
Notes: 介绍了加法器——CPU中的核心部件
如何使用加法器构建出二进制加法、减法、乘法功能

## Slide 2: Full Adder Logic Function
Inputs |  |  | Outputs | 
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1
Cout = 1: at least 2 out 3 of the (A, B, Cin) inputs are Logic 1
S = 1: odd number of the (A, B, Cin) inputs are Logic 1
Notes: 半加器和全加器，半加器可以作为全加器的特殊情况。
输入3，输出2，sum和carry

## Slide 3: Static CMOS Adder Version 1
𝑪𝒐𝒖𝒕 = 𝑨𝑩 + 𝑨 + 𝑩 𝑪𝒊𝒏
如何使用静态CMOS方法将其分别实现？
使用该方法实现的全加器，需要多少个晶体管？
44

## Slide 4: Full Adder – Another Look
It’s all about carry, so re-define terms for more efficient design.
使用A，B控制Cin
Carry status
  Delete (D)
  Propagate (P)
  Generate (G)
Full Adder
  Internally generates P, G, (D)
A | B | Cin | Cout | Cout Status
0 | 0 | 0 | 0 | D
0 | 0 | 1 | 0 | D
0 | 1 | 0 | 0 | P
0 | 1 | 1 | 1 | P
1 | 0 | 0 | 0 | P
1 | 0 | 1 | 1 | P
1 | 1 | 0 | 1 | G
1 | 1 | 1 | 1 | G
𝑷 = 𝑨⨁𝑩
𝑮 = 𝑨 ∙ 𝑩
𝑪𝒐𝒖𝒕 = 𝑫 ∙ 𝟎 + 𝑷 ∙ 𝑪𝒊𝒏 + 𝑮 ∙ 𝟏
𝑪𝒐𝒖𝒕 = 𝑷 ∙ 𝑪𝒊𝒏 + 𝑮

## Slide 5: Full Adder – Another Look
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Propagate
Generate
We can also derive expressions for S based on D and P
Delete

## Slide 6: Static CMOS Adder Version 2
𝑪𝒐𝒖𝒕 = 𝑷 ∙ 𝑪𝒊𝒏 + 𝑮
𝑷 = 𝑨⨁𝑩
𝑮 = 𝑨 ∙ 𝑩
𝑺 = 𝑷⨁𝑪𝒊𝒏
Preparation Stage
需要使用多少个晶体管？（38）

## Slide 7: Full Adder – A Third Look
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
𝑪𝒐𝒖𝒕 = 𝑮 + 𝑷 ∙ 𝑪𝒊𝒏 = 𝑨𝑩 +
𝑨⨁𝑩
𝑪𝒊𝒏
Cout = 0, S = A + B + Cin
Cout controls A & B
Cout = 1, S = A  B  Cin
out
Eliminate XOR Gate
Integrate C and S
Most Brief Expression
𝑪𝒐𝒖𝒕 = 𝑨𝑩 +
𝑨 + 𝑩
𝑪𝒊𝒏
Notes: 之前的设计需要很多晶体管，因为异或太多

## Slide 8
希望大家给五星满分好评！