## Slide 1: Interconnection Network

## Slide 2: Interconnection Networks[互连网络]
An Interconnection Network (ICN) is a programmable system that transports data between terminals
  To hold our parallel machines together
    at the core of parallel computer architecture
  Share basic concept with LAN/WAN
  but very different trade-offs due to very different time scale/requirements

## Slide 3: Interconnection Networks[互连网络]
Interconnection networks can be grouped into four domains
  Depending on number and proximity of devices to be
    Wide-Area Networks[广域网]
    Local-Area Networks[局域网]
    System-Area Networks[系统区域网络]
    On-Chip Networks[片上网络]

## Slide 4: Wide-Area Networks
Interconnect systems distributed across the globe
  Internetworking support is required
  Millions of devices interconnected
Maximum interconnect distance
  many thousands of kilometers

## Slide 5: Local-Area Networks
Interconnect autonomous computer systems
  Machine room or throughout a building or campus
  Hundreds of devices interconnected
Maximum interconnect distance
  Few meters to tens of kilometers
  Example (most popular):
    Ethernet, with 10 Gbps over 40Km

## Slide 6: System-Area Networks
Interconnects within one “machine”
  Interconnect in a multi-processor system
  Interconnect in a supercomputer
  Hundreds to thousands of devices interconnected
    Tianhe-2 supercomputer (16K nodes)
Maximum interconnect distance
  Fraction to tens of meters (typical)
  A few hundred meters (some)
    InfiniBand: 120 Gbps over a distance of 300m
Notes: InfiniBand is a high-speed, low-latency interconnect technology primarily used in high-performance computing (HPC) environments, such as supercomputers, data centers, and high-speed networks. 1. High Bandwidth: InfiniBand offers high data transfer rates, ranging from gigabits per second (Gbps) to terabits per second (Tbps), depending on the generation and configuration.
Low Latency: InfiniBand provides low-latency communication, which is crucial for applications requiring real-time data processing and high-performance computing tasks.
Scalability: InfiniBand supports large-scale deployments and can scale to thousands of nodes in a single fabric, making it suitable for demanding workloads and distributed computing environments.
Reliability: InfiniBand offers features such as error detection, correction, and fault tolerance mechanisms to ensure data integrity and reliability.
Remote Direct Memory Access (RDMA): One of the key features of InfiniBand is RDMA, which allows data to be transferred directly between the memory of one computer and another without involving the CPU. This can significantly reduce latency and CPU overhead, improving overall system performance.

## Slide 7: System-Area Networks
Notes: APM (Application Performance Management)

## Slide 8: On-Chip Networks
Interconnect within a single chip
  Devices are micro-architectural elements
    Caches, directories, processor cores
  Currently, designs with tens of devices are common
    Ex: IBM Cell, Intel multicores, Tile processors
Proximity: millimeters
We are concerned with On-Chip and System-Area Networks

## Slide 9: Why Study Interconnects?
Provide external connectivity from system to outside world
  Also, connectivity within a single computer system at many levels
Interconnection networks should be well designed
  To transfer the maximum amount of information
  Within the least amount of time (and cost, power constraints)
Application:
  managing communication can be critical to performance

## Slide 10: Why Study Interconnects? (cont.)
Trends: high demand on communication bandwidth
  increased computing power and storage capacity
  switched networks are replacing buses
Computer architects/engineers must understand interconnect problems and solutions
  in order to effectively design and evaluate systems
Notes: https://zhuanlan.zhihu.com/p/346426970
In traditional bus-based network architectures, such as Ethernet networks using hubs, all devices on the network share the same communication medium (the bus). When a device sends data, it broadcasts it to all other devices on the network, and only the intended recipient processes the data, while others ignore it. This approach can lead to network congestion and reduced efficiency, especially as the number of devices on the network increases.
Switched networks, on the other hand, use network switches to facilitate communication between devices. Each device is connected to a switch, and the switch forwards data packets only to their intended destination based on the destination address. This approach reduces network congestion and improves efficiency by minimizing unnecessary broadcasts.

## Slide 11: Interconnection network
Characteristics of communication
  Latency must be low
  Bandwidth must be high
  Message characteristics
    Many small messages with several fixed sizes
    The largest message is one cache block size (64 or 128 bytes)
Implications
  Only two layers are sufficient: link level and node level
  Communication protocol must be simple
    no packet dropping, no elaborate flow control

## Slide 12: Nodes and Links
A node encapsulates
  one or more processors
  communication controller/assist (CA)
  router
  Routers are connected by links
  Links may be unidirectional or bidirectional

## Slide 13: Link and Channel
Link = set of wires interconnecting a pair of nodes
  Link can be unidirectional or bidirectional
  Unit of transfer determined by flow control protocol (flit)
  Flit size determined by link latency and amount of buffering available
Channel = link + sender + receiver
A message transmitted over a channel is broken into packets
  A packet has a header, trailer, and payload

## Slide 14: Design Considerations
Application requirements
  Number of terminals or ports to support
  Peak bandwidth of each terminal
  Average bandwidth of each terminal
  Latency requirements
  Message size distribution
  Expected traffic patterns
  Required quality of service
  Required reliability and availability

## Slide 15: Design Considerations
Job of an interconnection network:
  to transfer information from source node to dest. node
  support network transactions that realize application
Latency as small as possible
  As many concurrent transfers as possible
Cost as low as possible

## Slide 16: Example Requirements
Example requirements for a coherent processor-memory interconnect
  Processor ports 1-2048
  Memory ports 1-4096
  Peak BW 8 GB/s
  Average BW 400 MB/s
  Message Latency 100 ns
  Message size 64 or 576 bits
  Traffic pattern arbitrary
  Quality of service none
  Reliability no message loss
  Availability 0.999 to 0.99999

## Slide 17: Technology constraints
Technology constraints
  Signaling rate
  Chip pin count (if off-chip networking)
  Area constraints (typically for on-chip networking)
  Chip cost
  Circuit board cost (if backplane boards needed)
  Signals per circuit board
  Signals per cable
  Cable cost
  Cable length
  Channel and switch power constraints

## Slide 18: Off-chip vs. On-chip ICNs
Off-chip: I/O bottlenecks
  Pin-limited bandwidth
  Inherent overheads of off-chip I/O transmission
On-chip
  Wiring constraints
    Horizontal and vertical layout
    Short, fixed length
  Power
    Consume 10-15% or more of die power budget
  Latency
    Different order of magnitude

## Slide 19: Main Aspects of an ICN
Topology
  Static arrangement of channels and nodes in a network
Routing
  Determines the set of paths a packet can follow
Flow control[流控]
  Allocating network resources (channels, buffers, etc.) to packets and managing contention

## Slide 20: Main Aspects of an ICN
Switch microarchitecture
  Internal architecture of a network switch
Network interface
  How to interface a terminal with a switch
Link architecture
  Signaling technology and data representation on the channel

## Slide 21: 1. Network Topology

## Slide 22: Network Topology
Network topology = shape of the network
  Determines the distance that a message needs to travel (in # links or network hops) from one node to another
Important characteristics
  Diameter: largest distance
  Average distance
  Degree: how many links are connected to a switch

## Slide 23: Example
For the shown network, compute diameter, avg distance, bisection bandwidth (assuming each link is bidirectional)
Diameter = 3
e.g. the distance between node 1 and 6
Avg distance:
  d(1,2)=1, d(1,3)=2, d(1,4)=1, d(1,5)=2, d(1,6)=3
  d(2,3)=1, d(2,4)=2, d(2,5)=2, d(2,6)=2
  d(3,4)=2, d(3,5)=1, d(3,6)=1
  d(4,5)=1, d(4,6)=2
  d(5,6)=1
  Sum of all distances = 24, number of node pairs = 15
  Average distance = 24/15

## Slide 24: Recall: Shared Memory System

## Slide 25: Recall: Distributed Memory System

## Slide 26: Interconnection networks
Affects performance of both distributed and shared memory systems.
Two categories:
  Shared memory interconnects
  Distributed memory interconnects

## Slide 27: 1.1 Shared memory interconnects

## Slide 28: Shared memory interconnects
Bus interconnect
  A collection of parallel communication wires together with some hardware that controls access to the bus.
  Communication wires are shared by the devices that are connected to it.
  As the number of devices connected to the bus increases, contention for use of the bus increases, and performance decreases.

## Slide 29: Shared memory interconnects
Switched interconnect
  Uses switches to control the routing of data among the connected devices.
  Crossbar –
    Allows simultaneous communication among different devices.
    Faster than buses.
    But the cost of the switches and links is relatively high.

## Slide 30
(a)
A crossbar switch connecting 4 processors (Pi) and 4 memory modules (Mj)
(b)
Configuration of internal switches in a crossbar
(c) Simultaneous memory accesses by the processors

## Slide 31: 1.2 Distributed memory interconnects

## Slide 32: Distributed memory interconnects
Two groups
  Direct interconnect
    Each switch is directly connected to a processor memory pair, and the switches are connected to each other.
  Indirect interconnect
    Switches may not be directly connected to a processor.

## Slide 33: （1）Direct interconnect

## Slide 34: Direct interconnect
ring
toroidal mesh
（二维环面网格）
Notes: toroidal mesh 二维环面网格

## Slide 35: Bisection width（等分宽度）
A measure of “number of simultaneous communications” or “connectivity”.
How many simultaneous communications can take place “across the divide” between the halves?

## Slide 36: Two bisections of a ring
For toroidal mesh

## Slide 37: Definitions
Bandwidth
  The rate at which a link can transmit data.
    Usually given in megabits or megabytes per second.
Bisection bandwidth
  A measure of network quality.
  Instead of counting the number of links joining the halves, it sums the bandwidth of the links.

## Slide 38: Fully connected network
Each switch is directly connected to every other switch.
bisection width = p2/4
(p: # of nodes)
impractical
Notes: P: # of nodes.

## Slide 39: Hypercube
Highly connected direct interconnect.
Built inductively:
  A one-dimensional hypercube is a fully-connected system with two processors.
  A two-dimensional hypercube is built from two one-dimensional hypercubes by joining “corresponding” switches.
  Similarly a three-dimensional hypercube is built from two two-dimensional hypercubes.

## Slide 40: Hypercubes
one-
three-dimensional
two-

## Slide 41: （2）Indirect interconnect

## Slide 42: Indirect interconnects
Simple examples of indirect networks:
  Crossbar
  Omega network
Often shown with unidirectional links and a collection of processors
Each of which has an outgoing and an incoming link, and a switching network.

## Slide 43: A generic indirect network

## Slide 44: Crossbar interconnect for distributed memory

## Slide 45: An omega network

## Slide 46: A switch in an omega network

## Slide 47: More definitions
Any time data is transmitted, we’re interested in how long it will take for the data to reach its destination.
Latency
  The time that elapses between the source’s beginning to transmit the data and the destination’s starting to receive the first byte.
Bandwidth
  The rate at which the destination receives data after it has started to receive the first byte.

## Slide 48
Message transmission time = l + n / b
latency (seconds)
bandwidth (bytes per second)
length of message (bytes)

## Slide 49: 2. Routing Policy

## Slide 50: Routing policy
Store & Forward:
  Send all flits over a link, then over another, and so on
  T = h * (Txmit + Tswitch)
Cut-through:
  Send flits in pipeline over the links
  T = h * Tswitch + Txmit
Implication:
  cut-through routing reduces the importance of topology
How to send a packet over the network?

## Slide 51: Routing Policy
Minimal vs. non-minimal
  Minimal = each packet travels the least number of hops
Deterministic vs. non-deterministic
  Deterministic = each sender-dest pair uses a single path for all messages
Adaptive vs. non-adaptive
  Adaptive = message can change path as it is being transmitted
Deadlock-free vs. Deadlock possible
  Deadlock due to several messages mutually waiting for buffer space

## Slide 52: What is Deadlock?
Inability of the network to forward packets
  Due to limited buffer space and cyclic dependence on buffer acquisition
Handling a deadlock
  Detect and break: expensive
  Drop packets: adverse effect in performance and complicates protocol
  Avoid: restriction on routing
The figure shows four packets filling up the input buffer and need the next output buffer, but the output buffer is already full

## Slide 53: 3. Router Architecture

## Slide 54: Router Architecture
Router has four input ports and four output ports
Each channel has two virtual channels (VCs), with separate buffers

## Slide 55: Router Architecture
Arriving packet sent to the appropriate VC (buffer) based on its header
Control logic arbitrates among multiple input channels and allocates them to the input of the crossbar switch
  It also allocates output VC to the output of the switch
  It arbitrates multiple input ports that want to send packet to the same output port

## Slide 56: Router Architecture
Switch typically implemented using a crossbar (to minimize latency and collision)
  Multiple flits from different VCs can go on the switch as long as they go to different output VCs
Steps can also be pipelined to improve router throughput

## Slide 57: Summary
Interconnection network
  Basic concepts
  Design consideration
  Main aspects
Network Topology
Routing Policy
Router Architecture

## Slide 58: Cache coherence

## Slide 59: Recall that…
Caches are managed by system hardware
Out of a programmer’s direct control!
Any undesired consequence?

## Slide 60: What would happen?

## Slide 61: What would happen?
Suppose executed at the indicated times
What value z1 will get, 4*7=28 or 4*2=8?
Unpredictable! Whether write-through or write-back…

## Slide 62: Cache Coherence Problem
When the caches of multiple processors store the same variable, an update by one processor to the cached variable, how to ensure the cached value stored by the other processors is also updated.
  Snooping cache coherence
  Directory-based cache coherence

## Slide 63: 监听（Snooping）Cache Coherence
Notes: Source: https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.researchgate.net%2Ffigure%2FSnooping-based-cache-coherence_fig2_324599927&psig=AOvVaw23rpj0jdC8768InYpwTM0u&ust=1709610752742000&source=images&cd=vfe&opi=89978449&ved=0CBMQjRxqFwoTCKiY5r_a2YQDFQAAAAAdAAAAABAJ

## Slide 64: 基于目录的(Directory-based) Cache Coherence
Directory (a data structure) stores the status of each cache line
  Also support distributed-memory
  Directory is maintained in a distributed way
Notes: https://www.researchgate.net/publication/259821213/figure/fig4/AS:392548955770892@1470602372166/Organization-of-Directory-Based-Protocol.png

## Slide 65: 基于目录的(Directory-based) Cache Coherence
Pros: Substantial additional storage required for the directory
Cons: When a cache variable is updated, only the cores storing that variable need to be contacted

## Slide 66: 伪共享 (False Sharing)
Suppose , core_count = 2, each cache line is 64 bytes!
The system is behaving as if the elements of y were being shared by the cores !

## Slide 67: Supplementary materials

## Slide 68: Computing bisection width
back