## Slide 1: Directory-Based Cache Coherence

## Slide 2: Scalable Shared Memory System
Bus-based MP: good for small multiprocessors, but does not scale
  Physical constraints
    long wires (low clock frequency), arbitration delay
  Protocol constraints
    Snoopy/broadcast: bandwidth getting saturated quickly
  Contention everywhere:
    bus, snooper, memory
How to scale to larger MP?

## Slide 3: Scalable Shared Memory System
 |  | Interconnection | 
 |  | Bus | Point-to-Point
Protocol | Snoopy | Least scalable | More scalable
 | Directory | / | Most scalable

## Slide 4: Ways to Scale Bus-Based MP
Approach 1: replace bus with point-to-point interconnection, but keep relying on snooping/broadcast
  e.g., AMD Opteron (mesh), IBM Cell (ring), Intel Larrabee (ring)
  Still cannot scale to hundreds of processors

## Slide 5: Ways to Scale Bus-Based MP
Approach 2: replace broadcast with directory protocol
  e.g. SGI Altix system
  Leads to distributed shared memory (DSM) multiprocessors
  Scaling to tens to hundreds of processors

## Slide 6: Directory Protocols

## Slide 7: Questions to be considered
Questions:
  Which memory a block must be placed in
  Where the directory of a particular block can be found
  How the directory information is organized
  How to handle races in the protocol
  How to ensure write propagation and write serialization in a DSM
  …….

## Slide 8: Question 1
Q1: which memory to place a particular block?
One solution: block interleaving
Works against spatial locality of accesses
In most DSMs, block interleaving is not used.

## Slide 9: Question 1
Another solution: mapping without interleaving
  Consecutive physical page frames (pfr) are mapped to a memory.
OS must be involved in deciding where to allocate
  First touch
    Processor that first accesses it.
  round robin

## Slide 10: Finding a Block
A block can only map to a single memory
  This memory is referred to as the “home” of the block
The home memory keeps track of which caches may have the copy of a block
  in a structure called the “directory”

## Slide 11: Question 2
Q2: where is directory stored?
Solution:
  Cache-based directory
    Kept as a doubly linked list among multiple caches
    Maintaining the list is too complicated!
  Memory-based directory
    Keep directory in the main memory.
    Mainstream approach

## Slide 12: Centralized Directory
Use a centralized directory to keep track of every block
  Which caches have each block
  Dirty status of each block
Not scalable
  The directory receives requests from all processors
  Its central location is far away from most processors

## Slide 13: Distributed Directory
The directory is scattered at different nodes.
  Keep directory info of a block in home node
Notes: Figure 5.18 A directory is added to each node to implement cache coherence in a distributed-memory multiprocessor. In this case, a node is shown as a single multicore chip, and the directory information for the associated memory may reside either on or off the multicore. Each directory is responsible for tracking the caches that share the memory addresses of the portion of memory in the node. The coherence mechanism will handle both the maintenance of the directory information and any coherence actions needed within the multicore node.

## Slide 14: Basic Directory Handling of Load Request
Requestor (P1) sends a Read request to the Home (P2) of the block
The home looks up the directory to find out who has the block and in what state. Then it sends an intervention request to the current owner (P3)
The owner (P3) supplies the block to the requestor (P1) and may update the home as well

## Slide 15: Basic Directory Handling of a Write Req
Requestor (P1) sends a Write request to Home (P2)
Home finds out that P2 and P3 are currently sharers, then it sends invalidation messages to them
Sharers (P2 and P3) reply with Invalidation Acknowledgement to P1

## Slide 16: What Info in the Directory?
Information that must be kept at the directory
  Which caches are currently sharers or owner
  Which state the block is currently cached
Ideally, if the caches support MESI states, then the directory keeps MESI states as well, but:
  Transition from Exclusive to Modified in a cache is silent
  Hence, the directory cannot tell if a block is cached in Exclusive or Modified state

## Slide 17: What Info in the Directory
Hence, the directory may keep 3 states
  Shared (S)
    The block is cached cleanly, possibly by multiple caches
  Uncached (U)
    The block is uncached or cached in invalid state.
  Exclusive or Modified (EM)
    The block is either cached in Exclusive or Modified state in only one cache.

## Slide 18: Basic DSM Cache Coherence Protocol

## Slide 19: Example
Cache State: MESI
Directory: Full-bit Vector
3 States:
  EM (Exclusive or Modified)
  S (Shared)
  U (Uncached)

## Slide 20: Coherence Messages
Issued by requesting processor:
  Read:
    read request from a processor
  ReadX:
    read exclusive (write) request from a processor that does not have the block
  Upgr:
    upgrade request (from Shared to Modified), made by a processor that already has the block

## Slide 21: Coherence Messages
Issued by home node:
  ReplyD:
    home replies with data to requestor
  Reply:
    home replies not containing data
  Inv (Invalidation):
    Invalidation request sent by home node to sharers
  Int (Intervention):
    Intervention request sent by home to owner, asking owner to flush and change to Shared state.

## Slide 22: Coherence Messages
Issued by owner of a cache block:
  Flush:
    owner flushes data to home + requestor
  InvAck:
    sharer/owner ack Invalidation msg
  Ack:
    acknowledgement of receipt of non-invalidation msg

## Slide 23: State Transition at the Directory
Legend:
  <Request-type>(<requestor>) / <Reply-type>(<destination>)
  O = owner, A = requestor, Shr = sharers
The intervention request also contains the ID of the requester, so that the owner knows where to send the block.
The invalidation request also contains the ID of the requester, so that the owner knows where to send the block.
Notes: EM state:
if a read request is received, the new state will be shared, and an intervention request is sent to the owner of the block.
The intervention request also contains the ID of the requester, so that the owner knows where to send the block.
If a ReadX request is received, the directory needs to send an invalidation to the current owner. The invalidation request also contains the ID of the requester,
So that the owner knows where to send the block.

## Slide 24: Full-bit Vector Protocol Visualization
P1
Cache
Main
Memory
Dir Ctrl
Data
State
Sharers
Interconnection Network
P3
Dir Ctrl
P2
Dir Ctrl

## Slide 25
P1
Dir Ctrl
Interconnection Network
P3
Dir Ctrl
P2
X=1
Dir Ctrl
rd &X
X = 1
E
EM
100
U
000
Proc Action | State P1 | State P2 | State P3 | Dir State @Home | Network Msg | Hops
R1 | E | - | - | EM, 100 | Read (P1-> H), ReplyD (H->P1) | 2

## Slide 26
P1
Dir Ctrl
Interconnection Network
P3
Dir Ctrl
P2
X=1
Dir Ctrl
wr &X
X=2
X = 1
E
EM
100
X=2
M
Proc Action | State P1 | State P2 | State P3 | Dir State @Home | Network Msg | Hops
W1 | M | - | - | EM, 100 | - | 0

## Slide 27
P1
Dir Ctrl
Interconnection Network
P3
Dir Ctrl
P2
X=1
Dir Ctrl
X = 2
M
EM
100
Rd &X
Read
Int
S
Flush
Flush
S
101
X = 2
S
X=2
Proc Action | State P1 | State P2 | State P3 | Dir State @Home | Network Msg | Hops
R3 | S | - | S | S, 101 | Read (P3->H), Int (H->P1), Flush (P1->H, P3) | 3

## Slide 28
P1
Dir Ctrl
Interconnection Network
P3
Dir Ctrl
P2
X=2
Dir Ctrl
X = 2
S
S
101
Wr &X
X = 3
Upgr
Inv
I
EM
001
X = 2
S
X=3
M
InvAck
Reply
Proc Action | State P1 | State P2 | State P3 | Dir State @Home | Network Msg | Hops
W3 | I | - | M | EM, 001 | Upgr (P3->H), Reply (H->P3) // Inv (H->P1), InvAck(P1->P3) | 3

## Slide 29
P1
Dir Ctrl
Interconnection Network
P3
Dir Ctrl
P2
X=2
Dir Ctrl
X = 2
I
EM
001
X = 3
M
rd &X
Int
Flush
S
S
101
X=3
X=3
S
Proc Action | State P1 | State P2 | State P3 | Dir State @Home | Network Msg | Hops
R1 | S | - | S | S, 101 | Read (P1->H), Int (H->P3), Flush (P3->H, P1) | 3

## Slide 30
P1
Dir Ctrl
Interconnection Network
P3
Dir Ctrl
P2
X=3
Dir Ctrl
X = 3
S
S
101
X = 3
S
rd &X
Proc Action | State P1 | State P2 | State P3 | Dir State @Home | Network Msg | Hops
R3 | S | - | S | S, 101 | - | 0

## Slide 31
P1
Dir Ctrl
Interconnection Network
P3
Dir Ctrl
P2
X=3
Dir Ctrl
X = 3
S
S
101
X = 3
S
rd &X
Read
ReplyD
111
X = 3
S
Proc Action | State P1 | State P2 | State P3 | Dir State @Home | Network Msg | Hops
R2 | S | S | S | S, 111 | Read(P2->H), ReplyD(H->P2) | 2

## Slide 32: Summary of State Changes
Proc Action | State P1 | State P2 | State P3 | Dir State @Home | Network Msg | Hops
R1 | E | - | - | EM, 100 | Read (P1-> H), ReplyD (H->P1) | 2
W1 | M | - | - | EM, 100 | - | 0
R3 | S | - | S | S, 101 | Read (P3->H), Int (H->P1), Flush (P1->H, P3) | 3
W3 | I | - | M | EM, 001 | Upgr (P3->H), Reply (H->P3) // Inv (H->P1), InvAck(P1->P3) | 3
R1 | S | - | S | S, 101 | Read (P1->H), Int (H->P3), Flush (P3->H, P1) | 3
R3 | S | - | S | S, 101 | - | 0
R2 | S | S | S | S, 111 | Read(P2->H), ReplyD(H->P2) | 2

## Slide 33: Performance Criteria of Directory Schemes
Main criteria:
  Traffic on invalidations
  Latency of invalidations
  Storage overheads
Less important criteria:
  Traffic on interventions
  Latency of interventions
Invalidation involves multiple sharers vs. intervention involves a single owner
Note:
Invalidation:
Any  Invalid
Intervention:
Exclusive/Modified  Shared

## Slide 34: 课程内容
参考材料：
  Fundamentals of Parallel Computer Architecture. Chapter 11 “Distributed Shared Memory Multiprocessors”.